## Slide 1
Mission Definition
Turtle mission is defined by a file loaded onto SD card prior to mission. File contains:
  Magnetic Variation for mission area
  Calm water (“no current”) swim speed
  Time interval (in seconds) between surfacing for GPS position checks.
  Number of waypoints (WPTs) in mission
  Lat/Lon coordinates of each (WPT)
Notes: <number>

## Slide 2
Turtle Controller Software
Runs on Pi Zero, under Rasbpian OS
Takes initial GPS check to define “home”
Lat/Lon WPTs converted to UTM coordinates.
  Conversion algorithm gives UTM coordinates accurate to within 0.01 meters north and east (!)
  All navigation, current speed/direction calculations, etc. are performed with UTM coordinates.
Notes: <number>

## Slide 3
Turtle Controller Navigation
Navigates to WPT by:
  Computing next segment of route towards WPT
    ETE, ETA, course, estimated speed, estimated segment endpoint
      Course is corrected for current and magnetic variation
      Estimated speed derived from course and calm water speed corrected for current direction and speed.
Notes: <number>

## Slide 4
Turtle Controller GPS Check
Initiate GPS check at the end of route segment
When traveling for surfacing interval seconds, route segment is complete.
  Surface for GPS check
When surfaced:
  Get GPS location
  Calculate current speed and direction by comparing actual position to segment estimated position and speed.
Notes: <number>

## Slide 5
Turtle Controller AI
When calculating route segment ETE, compute:
  Estimated battery power remaining if route segment is traveled.
  Estimated battery power required to travel from end of route segment back to mission starting point (home).
Notes: <number>

## Slide 6
Turtle Controller AI (con’t)
If traveling to the end of the route segment would leave insufficient power to return from that point to home:
  Abort mission. Return to home.
  Otherwise, travel the route segment.
Notes: <number>